## Slide 1: LT9611 --- Product Brief 2-Port MIPI to HDMI1.4 Converter
LT9611 ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
Features
Dual-Port MIPI® DSI/CSI Receiver
  Compliant with D-PHY1.2 ,DSI1.2/CSI-2 1.00 and DCS 1.02.00
  1~2 Configurable Port
  1 Clock Lane and 1~4 Configurable Data Lanes
  80Mb/s~2Gb/s per Data Lane
  Data Port ,Data Lane and Polarity Swapping
  Internal Rterm Calibration with Less than 5% Error
  Programmable Equalization
  Burst Mode and Non-Burst Mode Supported
  Dual Port Odd-Even Mode and Left-Right Mode Supported
  Support up to 24-bit RGB and YUV Data Format
HDMI1.4 Transmitter
  Compliant with HDMI1.4 and HDCP1.4
  Resolution Up to 4K 30Hz
  Programmable output swing and pre-emphasis
  Fully hardware controlled or optional software controlled HDCP operations
  Integrated CEC controller
  Integrated EDID shadow RAM and embedded EDID
  5V tolerance DDC/HPD I/Os
  Both AC-coupling and DC-coupling Supported
Miscellaneous
  1.8V and 3.3V Power Supply
  Support 100KHz and 400KHz I2C Slave
  Support MIPI DCS Config
Support up to 8-CH SPDIF/I2S Audio Input
Embedded EEPROM for firmware HDCP keys optionally
Temperature Range: -40℃ ~ +85℃
64-pin QFN 7.5*7.5 package
Description
The LT9611 MIPI® DSI/CSI to HDMI1.4 bridge features a dual-port MIPI® D-PHY receiver front-end configuration with 4 data lanes per port operating at 2Gbps per data lane and a maximum input bandwidth of 16Gbps.
The bridge provides a HDMI data output with optional S/PDIF or 8-channel I2S serial audio input. Its high fidelity 8-channel I2S can transmit stereo up to a 192kHz sampling rate. The S/PDIF can carry stereo LPCM audio or compressed audio, including Dolby® Digital and DTS®. The LT9611 is fabricated in advanced CMOS process and implemented in a small outline 7.5mm x 7.5mm QFN64 package. This package is RoHS compliant and specified to operate from -40°C to +85°C.
Applications
Mobile systems
Cellular handsets
Digital video cameras
Digital still cameras
Personal media players
Gaming
Camera systems
www.lontiumsemi.com

## Slide 2
LT9611 ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
HDMI1.4
Figure 1. LT9611 Typical Application Diagram
Ordering Information
Table 1. Ordering Information
Part Number | Operating Temperature Range | Package | Packing Method
LT9611 | -40°C to +85°C | QFN64 (7.5*7.5) | 
www.lontiumsemi.com

## Slide 3
LT9611 ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
Copyright © 2017 Lontium Semiconductor Corporation, All rights reserved.
Lontium Semiconductor Proprietary & Confidential
This document and the information it contains belong to Lontium Semiconductor. Any review, use, dissemination, distribution or copying of this document or its information outside the scope of a signed agreement with Lontium is strictly prohibited.
LONTIUM DISCLAIMS ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING THOSE OF NONINFRINGEMENT, MERCHANTABILITY, TITLE AND FITNESS FOR A PARTICULAR PURPOSE. CUSTOMERS EXPRESSLY ASSUME THEIR OWN RISH IN RELYING ON THIS DOCUMENT.
LONTIUM PRODUCTS ARE NOT DESIGNED OR INTENDED FOR USE IN LIFE SUPPORT APPLIANCES, DEVICES OR SYSTEMS WHERE A MALFUNCTION OF A LONTIUM DEVICE COULD RESULT IN A PERSONAL INJURY OR LOSS OF LIFE.
Lontium assumes no responsibility for any errors in this document, and makes no commitment to update the information contained herein. Lontium reserves the right to change or discontinue this document and the products it describes at any time, without notice. Other than as set forth in a separate, signed, written agreement, Lontium grants the user of this document no right, title or interest in the document, the information it contains or the intellectual property in embodies.
Trademarks Lontium™ 龙 迅 ™ and ClearEdge™ is a registered trademark of Lontium Semiconductor. All Other brand names, product names, trademarks, and registered trademarks contained herein are the property of their respective owners.
Visit our corporate web page at: www.lontiumsemi.com Technical support: support@lontium.com
Sales: sales@lontium.com
www.lontiumsemi.com